IP44  SALCOMBE OUTDOOR WALL LIGHTS

These instructions are provided for your safety.

Please read them carefully before commencing work and retain them for future reference.

SUITABLE FOR WALL MOUNT ONLY

These fittings should only be installed in normal non aggressive atmospheric locations to prevent rusting.  Aggressive environments to be avoided include locations by the sea,  polluted atmospheres or near heating flue outlets.

SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	Before installation and servicing disconnect the electricity supply at the fuse board.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*	This fitting should be fitted to a lighting supply protected by a 5 amp fuse or equivalent circuit breaker.

* 	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting.  Dispose of old bulbs carefully.

INSTALLATION

1.	Ensure the house electricity supply is off at the fuse board.

2.	If removing an existing fitting, first note down all wiring connections.

3.	Remove the front glass by removing the screws holding on the retaining frame.  Unscrew the thumb screw holding the wall mounting bracket to the backplate.  Fix the mounting bracket firmly to the wall.

| 4. Unscrew four screws holding cover onto box. | 5. Unclip connector block from inside box. | 6. Push small screwdriver through soft grommet in back of box. |
| --- | --- | --- |

7.	Feed supply cable from house supply through hole in soft grommet which will form a seal around the cable

8.	The weight of the fitting must be supported whilst you make the electrical connections.

Make all electrical connections through the connector block.

Ensure electrical connections are tight and no loose strands of wire are left out of the block.

Connect the live (brown) wire of the wall light to the supply live wire.

Connect the neutral (blue) wire of the wall light to the supply neutral wire.

Connect the earth (green/yellow) wire of the light to the supply earth (unsheathed or green/yellow).

9.	Ensure electrical connections are tight and no loose strands of wire are left out of the connector block.

10.	Replace cover on box.

11.	Fix the fitting onto the wall by ensuring the white seal is attached to the edge of the backplate.  Push wall bracket thread through hole in backplate and secure with thumb screw ensuring light is correct way up.

12.	To fit bulb:  Remove glass and cage by removing retaining screws.  Fit the bulb, type and wattage as indicated on the fitting. The wattage indicated must not be exceeded.  Replace glass and cage ensuring rubber sealing gasket is located under glass.

13.	Switch on the electricity supply at the fuse board.