LOFT LE GU10 WALL FITTINGS

(Only Use Low Energy Lamps)

INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read carefully before commencing work and retain for future reference.

SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	This fitting should be fitted in accordance with current IEE Wiring Regulations and Building Regulations.

*  	To prevent electrocution switch off at the mains supply before installing or maintaining this fitting. Ensure other persons cannot restore the electricity supply without your knowledge.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*      This fitting is Class II =      therefore no earth is required and should be fitted to a lighting supply protected by a 5 amp

fuse or equivalent circuit breaker.

* 	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting. Never exceed the wattage stated.

*  	When changing the bulb, always switch off at the mains and allow the old bulb to cool down before handling. Dispose of used bulbs carefully.

INSTALLATION

- Ensure the house electricity supply is off at the fuse board.

- If you are fitting this product in place of an existing one, you may find that there are more than 3 sets of cables connected within existing rose.  Before removing existing fitting, carefully note position of each set of cables.

- Remove mounting bracket from fitting by undoing retaining screws then, using as a template, mark and drill the fixing centres in the wall. Ensure that the holes are drilled into a joist or other suitable mounting.

- Attach mounting bracket onto the wall using suitable fixings. Ensure screws are firmly fixed into joist or other suitable mounting and not just the plaster. Take care not to damage wiring.

- Use a screw driver to lever open the connector block housing then feed supply cable through rubber sleeve and make electrical connections as follows: Note. Ensure any basic insulation on the supply cable is covered by the rubber sleeve.

Connect supply live (normally brown or red) to fitting live (marked “L”) on the terminal block.

Connect supply neutral (normally blue or black) to fitting neutral (marked “N”) on the terminal block.

Note: No earth should be connected to any part of this fitting. If an earth is present terminate these in a separate terminal block (not supplied) to ensure that continuity is maintained for the earth circuit.

Ensure electrical connections are tight and no loose strands of wire are left out of the connector block. Ensure terminals and rubber sleeve is correctly seated then close connector block housing.

- Ensure wires are carefully tidied inside fitting cup. Offer fitting over mounting bracket and align fixing holes, use screws removed earlier to secure fitting to mounting bracket. Take care not to trap wires in the process.

- Fit the bulb, type and wattage as indicated on the fitting, you may require the lamp fitting tool provided to ease fitment. The wattage indicated must not be exceeded.

- Switch on the electricity supply at the fuse board.

## GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness

in plaster or paint can damage the finish. Do not use polish or abrasive cleaner - just a soft dry cloth.

# Text boxes

Double Light Spot

(Wall Light)

These products are sold individually.