ARDECHE PENDANT

INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read carefully before commencing work and retain for future reference.

#### SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	This fitting should be fitted in accordance with IEE Wiring Regulations and the Building Regulations

*  	To prevent electrocution switch off at the mains supply before installing or maintaining this fitting. Ensure other persons cannot restore the electricity supply without your knowledge.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*	This fitting is Class I =  and should be fitted to a lighting supply (with earth) protected by a 5 amp fuse or equivalent circuit breaker.

*  	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting. Never exceed the wattage stated.

* 	When changing the bulb, always switch off at the mains and allow the old bulb to cool down before handling. Dispose of used bulbs carefully.

It would be advised to seek assistance when attaching this fitting to the ceiling as the glass is heavy and fragile. Take care to prevent injury or damage

ASSEMBLY

It is possible to adjust the length of the chain at this point. Using 2 pairs of pliers with a soft cloth between the jaws open up a link in the chain. Open up another link to remove the length of chain required and then close the links back up. Pull the excess cable up through the ceiling cup leaving the cable slightly slack through the chain. Ensure that it is the chain supporting the weight of the fitting and not the cable.

### INSTALLATION

- Ensure the house electricity supply is off at the fuse board.

- If you are fitting this product in place of an existing one, you may find that there are more than 3 sets of cables connected. If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting. Before removing existing fitting, carefully note position of each set of cables

- If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting.

- Remove the mounting bracket from the fitting by undoing the screws located on the sides of the ceiling cup

- Using the mounting bracket as a template mark and drill holes in the ceiling. Ensure that they are into a joist or other suitable mounting. Fix the mounting bracket to ceiling with suitable fixings. Take care not to damage wiring.

- You may require assistance at this point. Take care in the next steps as the glass is quite heavy and fragile.

- Use a small screwdriver to lever open the terminal block then feed supply cable through the rubber sleeve and make electrical connections as follows.

Connect supply live (normally brown or red) to terminal block marked ’L’ on fitting.

Connect supply neutral (normally blue or black) to terminal block marked ‘N’ on the fitting.

Connect the earth (normally green/yellow or unsheathed) to terminal block marked ‘ ‘on the fitting.

NOTE: Ensure electrical connections are tight and no loose strands of wire are left out of the connector block. Close terminal block by snapping covers back together.

- Attach fitting to the mounting bracket by using any screws and washers that were removed earlier. Take care not to trap any wiring in the process.

- Fit the bulb, type and wattage as indicated on the fitting. The wattage indicated must not be exceeded.

- Switch on the electricity supply at the fuse board.

GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness in

plaster or paint can damage the finish.  Do not use polish or abrasive cleaner - just a soft dry cloth.