ETERNITY LOW VOLTAGE PENDANT FITTINGS

INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read carefully before commencing work and retain for future reference.

# SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	This fitting should be fitted in accordance with IEE Wiring Regulations and the Building Regulations.

*  	To prevent electrocution switch off at the mains supply before installing or maintaining this fitting. Ensure other persons cannot restore the electricity supply without your knowledge.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*	This fitting is Class I =  and should be fitted to a lighting supply (with earth) protected by a 5 Amp fuse or equivalent circuit breaker.

* 	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting. Never exceed the wattage stated.

*  	When changing the bulb, always switch off at the mains and allow the old bulb to cool down before handling.  Dispose of used bulbs carefully.

*	This fitting is designed for use with self-shielded tungsten halogen lamps only.

Note: This product is fitted with an electronic transformer and is suitable for dimming only when used with a suitable trailing edge dimmer. Not all dimmers are suitable for this product. Only use a suitably rated trailing edge dimmer.

Replacement Transformers:	 10 Light Pendant - TRASET210CS, 6 Light Pendant – TRASET150CS.

# INSTALLATION

- Ensure the house electricity supply is off at the fuse board.

- Before removing the existing product, carefully note the position of each set of cables. If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting.

- Remove back plate from the fitting by loosening the three retaining screws around the rim of the ceiling cup.(

- Firmly hold the stem, near the threaded section, and screw into the central sphere. Ensure stem is fully tightened.(a. Note: Do not attempt to arrange the decorative rings at this stage.

- Using back plate as a template, mark and drill fixing holes in the ceiling. Ensure fixing holes are located in a joist or other suitable surface. Feed supply cable through the back plate then attach back plate to the ceiling using suitable screws.(

- Telescopic Pendant Only: This is not a “rise and fall” pendant. Height must be set during installation. This product is fitted with a ‘telescopic’ adjustment stem.( Use the Allen key provided to completely undo the grub screws located at the bottom of the thicker stem. Adjust the height as required then secure in position by fully tightening the grub screws. Note: There will be indentation marks where the grub screw has been tightened.

- The weight of the fitting must be supported whilst making the electrical connections as follows: (a.

Connect the supply live (normally brown or red) to fitting live (marked “L”) on the terminal block.

Connect the supply neutral (normally blue or black) to fitting neutral (marked “N”) on the terminal block.

Connect the supply earth (normally green/yellow or unsheathed) to earth (marked “”) on terminal block.

NOTE: Ensure electrical connections are tight and no loose strands of wire are left out of the terminal block.

- Offer fitting up to the back plate. Align slots in ceiling cup rim with back plate retaining screws. Turn ceiling cup clockwise until a stop is reached. Secure ceiling cup by tightening the retaining screws.(b Take care not to trap the wiring.

- To minimise packaging waste, product is delivered with all decorative rings in the same plane (flat). Carefully undo the domed nuts located at the pivot points then use a spanner to loosen the nuts. Adjust each ring in turn, starting with central ring, then tighten the fixing nuts. Ensure central ring does not contact bulbs or bulb holders as this may damage them. Replace the domed nuts.(b.

- Fit the bulb: Type and wattage as indicated on the fitting.( The wattage indicated must not be exceeded. Use only self-shielded bulbs.   Do not touch halogen bulbs with bare hands, as this will shorten their life.

- Switch on the electricity supply at the fuse board.

## GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness

in plaster or paint can damage the finish.  Do not use polish or abrasive cleaner - just a soft dry cloth.

ETERNITY LOW VOLTAGE PENDANT FITTINGS

# Text boxes

This diagram is offered as a guide. Please follow all the safety and installation information overleaf.

6 Light Pendant.

10 Light Telescopic Pendant.

Telescopic Pendant Only.

These products are sold individually.

These products are sold individually.