GU10 FITTING INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read them carefully before commencing work and retain them for future reference.

SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	Before installation and servicing disconnect the electricity supply at the fuse board.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*	This fitting should be fitted to a lighting supply (with earth) protected by a 5 amp fuse or equivalent circuit breaker.

* 	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting.

*   The fitting should be installed so the bulb is no closer than 30cm from the surface it is illuminating.

# INSTALLATION

1.	Ensure the house electricity supply is off at the fuse board.

2.	If you are fitting this unit in place of an existing ceiling rose, you may find that there are more than 3 sets of cables connected within the rose.  Before removing the existing rose, carefully note the position of each set of cables.  If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting.

- Using the fitting as a template, mark and then drill the fixing holes in the ceiling or wall (ensure that the holes are drilled into a joist and not just the plaster).

- Remove the bracket from the fitting and attach the bracket to the wall or ceiling with suitable screws.  Do not attach fitting to the bracket at this stage. Take care not to damage wiring.

5.	The weight of the fitting must be supported whilst you make the electrical connections.

The connector block inside the plate can be removed from the backplate for ease of wiring. Ensure electrical connections are tight and no loose strands of wire are left out of the connector block.  If the connector block is left loose, cover it and any adjacent wiring with a good quality insulation tape.

Connect the live (marked “L” or brown) wire of the fitting to the supply live (normally red).

Connect the neutral (marked “N” or blue) wire of the fitting to the supply neutral (normally black).

Connect the earth (green/yellow) wire of the fitting to the supply earth (normally unsheathed or green/yellow).

- Attach the fitting to the backplate using the screws provided.

- Fit the bulb(s) type and wattage as indicated on the fitting.

Always use self shielded bulbs.

Adjust the heads so they are no closer than 0.3m from illuminated surfaces to prevent overheating.

8.	Switch on the electricity supply at the fuse board.

GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness in plaster or paint can damage the finish.  Do not use polish or abrasive cleaner - just a soft dry cloth.