HYPERION CRYSTAL WALL LIGHT

INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read carefully before commencing work and retain for future reference.

# SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	This fitting should be fitted in accordance with IEE Wiring Regulations and the Building Regulations

*  	To prevent electrocution switch off at the mains supply before installing or maintaining this fitting. Ensure other persons cannot restore the electricity supply without your knowledge.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*	This fitting is Class 1 =  and should be fitted to a lighting supply (with earth) protected by a 5 amp fuse or equivalent circuit breaker.

* 	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting. Never exceed the wattage stated.

*  	When changing the bulb, always switch off at the mains and allow the old bulb to cool down before handling.  Dispose of used bulbs carefully.

# INSTALLATION

- Ensure the house electricity supply is off at the fuse board.

- Before removing the existing product, carefully note the position of each set of cables. If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting.

- Remove mounting bracket from the fitting by undoing 2 screws on the side of fitting rose and retain screws.

- Using mounting bracket as a template, mark and then drill the fixing holes in the wall.  Ensure fixing holes are located on a solid or suitable surface and not just plaster.

- Attach mounting bracket to the wall using suitable fixings and ensure screws are firmly fixed into joist or other suitable mounting and not just the plasterboard.

- Weight of the fitting must be supported whilst you make electrical connections.

Connect the supply live (normally brown or red) to fitting live (marked “L”) on the terminal block.

Connect the supply neutral (normally blue or black) to fitting neutral (marked “N”) on the terminal block.

Connect the supply earth (normally green/yellow or unsheathed) to earth (marked “”) on terminal block.

NOTE: Ensure electrical connections are tight and no loose strands of wire are left out of the terminal block.

- Offer wall fitting over mounting bracket then align fixing holes and secure in place with screws removed earlier. Take care not to damage wiring.

- Fit crystal scones by offering over the lamp holders then fit candle drops over lamp holders and make sure they are seated correctly.

- Fit clear droppers onto lighting arms by fitting the ring through fixing loops provided.

- Fit the bulb type and wattage as indicated on the fitting. The wattage indicated must not be exceeded.

- Switch on the electricity supply at the fuse board.

GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness in plaster or paint can damage the finish.  Do not use polish or abrasive cleaner - just a soft dry cloth.