LEXINGTON DUAL MOUNT CEILING FITTING

INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read carefully before commencing work and retain for future reference.

##### SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	This fitting should be fitted in accordance with IEE Wiring Regulations and the Building Regulations

*  	To prevent electrocution switch off at the mains supply before installing or maintaining this fitting. Ensure other persons cannot restore the electricity supply without your knowledge.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*    This fitting is Class 2 =          therefore no earth is required and should be fitted to a lighting supply protected by a 5 amp

fuse or equivalent circuit breaker.

*  	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting. Never exceed the wattage stated.

* 	When changing the bulb, always switch off at the mains and allow the old bulb to cool down before handling.  Dispose of used bulbs carefully.

# INSTALLATION

- Ensure the house electricity supply is off at the fuse board.

- Before removing the existing rose, carefully note the position of each set of cables. If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting.

- Screw the stem into main body of fitting and secure using the 2 grub screws and Allen key provided.

- Remove mounting bracket from fitting by undoing retaining screws. Using the bracket as a template, mark and then drill the fixing holes in the ceiling. ( Ensure that the holes are drilled into a joist or other suitable mounting and not just the plaster

- Fix the mounting bracket to ceiling using suitable fixings. Take care not to damage wiring.

- Chain links may be adjusted to reduce the height of the fitting. Using two pairs of pliers, carefully open the chain links and remove the required number of links. Close the links. Note: Cloth should be used between the jaws of the pliers to protect the decorative finish. Pull any excess cable through the ceiling cup; making sure the chain is supporting the weight of the fitting and not the cable

- Weight of the fitting must be supported whilst you make the make electrical connections as follows: (

Open connector using a screwdriver to lever open the casing. Feed the supply cable through the rubber sleeving:

Note. Ensure that any basic insulation on the supply cable is covered by the rubber sleeve.

Connect supply live (normally brown or red) to fitting live (marked “L”) on the terminal block.

Connect supply neutral (normally blue or black) to fitting neutral (marked “N”) on the terminal block.

The product is double insulated and no wire should be connected to the earth supply. All supply earth wires should be connected together into a single terminal block (not supplied) to maintain continuity of the earth circuit and isolated from the fitting by wrapping terminal block in two layers of good quality insulation tape.

Snap connector cover closed ensuring that the connections are sound and no lose strands of wire are exposed.

- Attach the fitting to the mounting bracket using the retaining screws removed earlier. (  Take care not to trap wires in the process.

- Fit the Shade (purchased separately). Remove the shade ring, fit the shade and secure with ring. Fit the bulb, type and wattage as indicated on the fitting. ( The wattage indicated must not be exceeded.

- Switch on the electricity supply at the fuse board.

#### GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness in plaster or paint can damage the finish. Do not use polish or abrasive cleaner - just a soft dry cloth.

###### LEXINGTON  PENDANT CONVERSION TO SEMI FLUSH

This product is supplied as a pendant fitting, follow the steps below to convert into a semi flush fitting.

You will require a spanner and a screwdriver (not supplied) for this conversion.

- Remove the mounting bracket from the fitting by removing the 2 fixing screws.(

- Use a small screwdriver to undo the wires attached to the terminal block then gently withdraw wires from terminal block. (

- Hold the ceiling cup firmly then use a spanner (not supplied) to undo the nut inside ceiling cup. Retain any washers and the earth for later. (

- Gently unwind cable from the chain links and take care not to pull cable.

- Once cable is free from chain links hold the short stem on the fitting firmly then turn the last loop in the chain, take care not to damage the wire. (

- Attach the ceiling cup, earth wire, shake-proof washer, terminal block plate and shake-proof washer then secure in place with the nut removed earlier. ( Tighten fully with a spanner.

- If it is not possible to fit excess cable into ceiling void, cut the cable and prepare wires then reconnect into terminal block. ( (Take care not to cut into inner cable sheath)

- Follow installation instructions as detailed overleaf.

# Text boxes

SHADES SOLD SEPARATELY

SHADES ARE SOLD SEPERATELY, THE SHADES SHOWN ARE FOR ILLUSTRATION PURPOSES ONLY

SHADES ARE SOLD SEPERATELY, THE SHADES SHOWN ARE FOR ILLUSTRATION PURPOSES ONLY