CYNTHIA G9 CEILING FITTING

INSTALLATION INSTRUCTIONS

These instructions are provided for your safety.

Please read carefully before commencing work and retain for future reference.

#### SAFETY INFORMATION

*	If you are in any doubt consult a person competent to give advice on the installation of electrical equipment.

*	This fitting should be fitted in accordance with IEE Wiring Regulations and the Building Regulations

*  	To prevent electrocution switch off at the mains supply before installing or maintaining this fitting. Ensure other persons cannot restore the electricity supply without your knowledge.

* 	To avoid damage to concealed wiring during installation, establish the direction of the supply cable before drilling fixing holes.

*  	This fitting is Class I =  and should be fitted to a lighting supply (with earth) protected by a 5 amp fuse or equivalent circuit breaker.

*  	Always be sure to use the correct type and wattage of bulbs as indicated on the fitting. Never exceed the wattage stated.

* 	When changing the bulb, always switch off at the mains and allow the old bulb to cool down before handling. Dispose of used bulbs carefully.

*  	This fitting is designed for use with self-shielded tungsten halogen lamps only =

### CEILING LIGHT ASSEMBLY

- The 3 and 5 light fittings are supplied collapsed to reduce packaging waste.

- Screw the central stem into the base of the fitting and tighten by hand.

- Secure the stem into position by tightening the grub screw on the stem with Allen key provided.

### INSTALLATION

- Ensure the house electricity supply is off at the fuse board.

- If you are fitting this product in place of an existing one, you may find that there are more than 3 sets of cables connected. If there are loop in cables that are not connected to the light these must be terminated in a separate terminal block not connected to the fitting. Before removing existing fitting, carefully note position of each set of cables

- Remove the mounting bracket from fitting by undoing retaining screws. Use as a template, mark and then drill the fixing holes in the ceiling (ensure that the holes are drilled into a joist or other suitable mounting and not just the plaster).

- Fix the mounting bracket to ceiling with suitable fixings. Take care not to damage wiring.

- Use a screwdriver to lever open the connector block housing and feed supply cable through rubber sleeve. The weight of the fitting must be supported whilst making the electrical connections as follows:

Connect the supply live (normally brown or red) to fitting live (marked “L”) on the terminal block.

Connect the supply neutral (normally blue or black) to fitting neutral (marked “N”) on the terminal block.

Connect the supply earth (normally green/yellow or unsheathed) to earth (marked “”) on terminal block.

Ensure electrical connections are tight and no loose strands of wire are left out of the connector block. Ensure terminals and rubber sleeve are correctly seated then close connector block housing.

- Offer fitting to mounting bracket and align fixing holes, use the screws and any washers removed earlier to secure fitting to the mounting bracket. Take care not to trap wiring in the process.

- Fit the bulbs, type and wattage as indicated on the fitting. The wattage indicated must not be exceeded. Use only self shielded bulbs.   Do not touch halogen bulbs with bare hands as this will shorten their life.

- To fit the glass:  Remove the shade ring from the lampholder then fit the glass in place and secure with shade ring, use shade fitting tool.

- Switch on the electricity supply at the fuse board.

GENERAL INFORMATION

This fitting is designed for internal use only and must be fitted to a DRY SURFACE as any dampness in

plaster or paint can damage the finish.  Do not use polish or abrasive cleaner - just a soft dry cloth.

# Text boxes

CYNTHIA 3 LIGHT AND 5 LIGHT FITTING